## Slide 1: Electricity and circuits
Notes: This lesson introduces the topic of electricity in general, and its practical applications. It includes the concepts of electric current and its unit, electric circuits, and schematic diagrams for circuit elements, and distinguishes between open circuits, closed circuits, and short circuits.

## Slide 2: Objectives
Define electric current.
Identify the electric symbols for basic circuit elements.
Identify and construct open, closed, and short circuits.
Notes: Tell students they will be learning some of the basic, practical information that is used by real electricians and electrical engineers.

## Slide 3
Which statement below is a correct definition of electric current? Electric current is:
  the energy of moving electrical charges.
  the flow of electric charges through a wire or circuit.
  the number of electrons in a circuit element.
  the attraction between charged particles in a wire.
Assessment
Notes: Answers to the assessment questions appear at the end of the presentation.

## Slide 4
Label each of these electrical symbols with the name of the electrical component it represents: battery; resistor; lamp; switch; or wire.
Assessment
Notes: Students usually enjoy learning to draw schematic diagrams using these standard symbols.

## Slide 5
Assessment
Identify the following circuits:
Notes: Circuit diagrams like these are standard everywhere. By the end of this lesson the students will know how to draw these diagrams, and what these symbols represent.

## Slide 6
electric current
ampere (A)
electric circuit
open circuit
closed circuit
short circuit
Physics terms
Notes: The ampere is the unit of electric current. The students will be using the ampere throughout this unit. You might prompt the students to think of what other units they expect to encounter. Perhaps they will mention volts, ohms, or watts.

## Slide 7
Legend has it that Benjamin Franklin flew his metal key on his kite in a lightning storm.
Do you think the story is true? Why or why not?
Ben Franklin and his kite
Notes: Benjamin Franklin suggested this experiment, but it is unclear from his notes whether he ever attempted some version of it. To try this in an actual lightning storm would be to risk death by electrocution. If he performed this experiment, he was lucky to survive it.

## Slide 8
Electricity is the flow of electric charges, typically through wires, conductors, and electrical devices.
Sometimes we can see the effects of electricity in nature.
What is electricity?
Notes: Ask the students for a couple of examples of static electricity in their everyday lives. When scientists first started learning about electricity, they did not know how to create currents in the laboratory. They could only create static charges.

## Slide 9
How do we use electricity?
Many household appliances and personal devices use electricity.
The room you are in right now is probably full of devices that use electricity.
Notes: Ask the students for examples of electricity use in the room where you are working. This will help students appreciate the ways that this topic is relevant to their lives.

## Slide 10
What is electric current?
Current is measured in amperes (A), also called amps.
Electric current is the flow of charged particles, usually through wires and circuits.
Animated illustration, page 472
Notes: See page 472 for this mouse-over animated illustration. Water current can be measured as the amount of water that flows past a certain point in a pipe every second. Electric current is a measure of the amount of electric charge that flows through a certain point in a wire every second. The charges are always in the wires, but there is only a current if the charges flow along the wire.

## Slide 11
How do we measure electric current?
Electric current is measured using an ammeter or, more commonly, a digital multimeter. Current sensors provide an additional way to measure current.
In order to properly measure current, all the current must flow into the meter and back out again, into the circuit being tested.
Notes: In other words, the multimeter must be connected in series.

## Slide 12
In this circuit, I = 0.3 amps.
What is an electric circuit?
An electric circuit is a conducting path through which electric current can flow.
The symbol for electric current is I.

## Slide 13
Build a human circuit
Stand up and form a circle around the edge of the classroom.
The circular path represents the wire of a circuit.
Each student represents a packet of mobile charge.
Notice that the charges are already in the wire! How did they get there?
Notes: Students often think that charges “come from” the battery. Point out that the mobile electrons are part of the wire itself. The wire is made of atoms, which are made of electrons and protons. Some of these electrons in a metal lie in the conduction band and are free to move about, unbound to any specific atom.

## Slide 14
GO:
STOP:
Build a human circuit
Close the imaginary switch so the “charges” start flowing around the circuit. “Charges” should not bunch up. Why not?
Students assigned to be “ammeters” should stand still and count the “charges” that pass that point in the circuit.
After 60 seconds, open the “switch” to stop the current flow.
“Ammeters” should report their measured currents. What should be true about these values? Why?
REPORT:
Notes: Students represent packets of like charges, so they repel each other. The ammeters should both report the same amount of current flow ( in students per minute ). Point out that in a circuit with a single branch, the charges have no choice but to stay in the wire. So the current must be the same everywhere in the wire, because the charges in a circuit are never created or destroyed.

## Slide 15
Charge is conserved
Electric current I must be the same at all points in a simple, single-loop circuit.
Charge can never be created or destroyed. All the charge that flows through one point in the circuit must flow through the next point also.
I
I
Notes: To get them ready for the next slide, ask “What kinds of parts might we need to build a circuit in the classroom?”

## Slide 16
An open circuit does not have a complete path so no current flows.
A closed circuit has a complete path, allowing current to flow.
Open and closed circuits
Notes: Point out the direction of the current arrow in the closed circuit, which shows current flowing from the positive battery terminal toward the negative terminal. This is called the “conventional current” direction, and is the direction that positive charges would flow through the circuit. Students will use this convention throughout the unit. In fact, it is actually the electrons that flow, and they flow in the opposite direction.

## Slide 17
Common circuit elements
Notes: Draw the students’ attention to the electrical symbol for each component. Point out the long and short slashes on the battery symbol, representing the + and – terminals. A battery can be represented by one or more sets of these slashes. Reassure them that they will be learning about resistors soon, but not in this lesson.

## Slide 18
Knife blade switches
A knife blade switch uses a mechanical lever to open/close a circuit connection.
The handle is an insulator, so you won’t get a shock when you touch it!
When attaching a knife blade switch to a circuit, do so with it in the open position.
Notes: The current flows much more easily through a simple wire than it does through the bulb and resistors. So when the switch is closed the current takes the easy way around and almost no current at all will flow through the other three paths.

## Slide 19
What is a short circuit?
Notes: The current flows much more easily through a simple wire than it does through the bulb and resistors. So when the switch is closed the current takes the easy way around and almost no current at all will flow through the other three paths.

## Slide 20
In Investigation 17A you will build electric circuits using the Modular Circuits kit.
Exploring the ideas
Notes: In this investigation, the students will find out how the Modular Circuits kit works, create a simple circuit, and then modify that circuit to create an open circuit, closed circuit, and short circuit.

## Slide 21
Investigation
Connect a battery, bulb, and four wire corners together to create the circuit in the diagram.
Add six jumpers to your circuit to connect the components together and make the bulb light up.

## Slide 22
Investigation
Questions
Remove a jumper. Why does the bulb not light up when the jumpers are not inserted?
Remove the battery module from the circuit, turn it upside down, and reconnect it. Does the bulb still light up? What do you think reversing the battery changes in the circuit?

## Slide 23
Investigation
Questions
Connect the two jumpers on the bulb module with a bare wire to create a short circuit. What happens to the bulb when you create a short circuit? Try connecting jumpers on the wire and battery modules. Does connecting any two jumpers create a short circuit?

## Slide 24
Investigation
Questions
Add a switch and any necessary wire modules to your circuit so that you can turn on and turn off the light by opening and closing the switch. Draw a circuit diagram of your new circuit, using the circuit symbols.
Describe another way you can create an open circuit without opening the switch.

## Slide 25
Assessment
Which statement below is a correct definition of electric current? Electric current is:
  the energy of moving electrical charges.
  the flow of electric charges through a wire or circuit.
  the number of electrons in a circuit element.
  the attraction between charged particles in a wire.
Notes: Remind students of the analogy between water and electricity made earlier in the presentation.

## Slide 26
Assessment
Which statement below is a correct definition of electric current? Electric current is:
  the energy of moving electrical charges.
  the flow of electric charges through a wire or circuit.
  the number of electrons in a circuit element.
  the attraction between charged particles in a wire.
Notes: Ask students to give an example of a large water current and a small water current. For example, the Mississippi River has a large current and a faucet has a small current. Ask for examples of large and small electric currents.

## Slide 27
Assessment
Label each of these electrical symbols with the name of the electrical component it represents: battery, resistor, lamp, switch, or wire.
Notes: The shape of the electrical symbol usually helps the students remember its function.

## Slide 28
wire switch battery lamp resistor
Assessment
Label each of these electrical symbols with the name of the electrical component it represents: battery, resistor, lamp, switch, or wire.
Notes: The shape of the electrical symbol usually helps the students remember its function.
28

## Slide 29
Assessment
Identify the following circuits:
Notes: Ask the students which circuit will have the highest current. Which will have the lowest (or no) current? Why?

## Slide 30
Assessment
Short circuit
Open circuit
Closed circuit
Identify the following circuits:
Notes: Ask the students which of these circuits can be dangerous, and why.
Answer: a short circuit can lead to overheating, which can cause a fire.