## Slide 1: Resistance and Ohm’s law
Notes: The lesson defines conductors and insulators, and introduces the concept of resistance. In most circuits, resistance is key to determining how much current will flow. Ohm’s law is the equation that allows us to relate the three variables of voltage, current, and resistance. An interactive calculator aids in applying Ohm's law for problem solving. In the investigation, students construct a resistor circuit and measure current as a function of resistance to explore the proportional relationships of Ohm's law.

## Slide 2: Objectives
Characterize materials as conductors or insulators based on their electrical properties.
State and apply Ohm’s law to calculate current, voltage or resistance in an electric circuit involving a single resistor.
Demonstrate the use of current and voltage sensors, power supplies, and resistors.
Notes: This lesson contains practical objectives in the use of lab equipment as well as objectives involving basic knowledge and mathematical application of formulas.

## Slide 3: Assessment
Which materials listed below are conductors?
  aluminum
  rubber
  copper
  gold
  diamond
Notes: Some students may already know which materials are conductors. Urge them to hold their answers until the end of the lesson.

## Slide 4: Assessment
A.
B.
C.
D.
Which equation below is incorrect?
Notes: Give students time to work through the four possibilities.

## Slide 5: Assessment
What is the voltage drop across a 50 Ω resistor when a current of 0.10 A flows through it?
What is the current through a 10 Ω resistor when it is connected directly to a 15 V battery?
How do you connect a voltmeter to measure the voltage across a circuit element?
Notes: Students will use the interactive calculator to explore the mathematical relationships between V, I and R.

## Slide 6
Did you successfully demonstrate the use of current and voltage and sensors, power supplies, and resistors?
Assessment

## Slide 7
resistance
resistor
ohm (Ω)
electrical conductor
electrical insulator
Physics terms
Notes: Point out the Greek letter omega, which can be used to represent the ohm unit.

## Slide 8
Ohm’s law:
Equations
Notes: There is only one key equation for this lesson. It is presented as part of the introduction to the lesson. Its meaning will be explained later.

## Slide 9
Electricity is all around us, yet we are not electrocuted on a daily basis. Why not?
Electrical conductors
Some materials are good electrical conductors, while others are good insulators.
Air, plastic, glass, wood, and rubber are all good insulators.
Notes: Prompt the students for more examples of insulators. How about conductors?

## Slide 10
A typical electrical wire has copper on the inside and plastic insulation on the outside.
Electrical wire
Copper is a good conductor because it has many electrons that are free to move through the material.
The plastic covering on the wire protects us from getting electrocuted.
Notes: To have a practical, working circuit, we need a complete conducting path, protected by a insulator, to prevent short circuits.

## Slide 11
... which is why you should never use electrical devices in or near a bathtub or shower!
Water is conductive too!
Ordinary tap water may conduct electricity ...
Notes: Ask: “What happens at the beach or pool when the lifeguards hear thunder?”

## Slide 12
How much current?
This lamp conducts electricity.
When the lamp is connected to a 10 V source, 2 amps of current flows through it.
But why? What determines how much current will flow?

## Slide 13
The lamp itself helps determine the current flow. Is the lamp filament a good conductor, or does it resist the flow of current?
How much current?
This lamp conducts electricity.
When the lamp is connected to a 10 V source, 2 amps of current flows through it.
But why? What determines how much current will flow?

## Slide 14
Resistance
Some materials are better conductors than others. How do we quantify this difference?
Electrical resistance R is a measure of how hard it is for electricity to flow through a material.
  Resistance is measured in ohms (Ω).
    [Ω is the Greek letter “Omega.”]
Notes: In this lesson the students will measure resistance indirectly by measuring current and voltage, and applying Ohm’s law.

## Slide 15
Electric circuit elements that have resistance are called resistors.
Resistors control the flow of current in a circuit.
Light bulbs have resistance, too.
Resistors
Notes: Resistors come in many sizes, but these resistors have the typical cylindrical shape and colored resister code found in commonly-used devices.

## Slide 16
Electric circuit elements that have resistance are called resistors.
Resistors control the flow of current in a circuit.
Light bulbs have resistance, too.
    The symbol for a resistor in a circuit is a zigzag line.
Resistors

## Slide 17
Resistance: an analogy
Notes: This animated illustration is found on page 480.

## Slide 18
Resistance: an analogy
Notes: Note that the “current” of water that flowed out of the second bottle is much greater. This can also be demonstrated with a common type of water spritzer with an adjustable nozzle.

## Slide 19
Ohm’s law relates electric current to the voltage and resistance.
Ohm’s law
Notes: Ohm’s law is description of the relationship between V, I and R in most materials. Some materials, such as semiconductors, are not “ohmic.”

## Slide 20
The current through a resistor will
increase if the voltage increases
decrease if the resistance increases
Ohm’s law relates electric current to the voltage and resistance.
The meaning of Ohm’s law
Notes: This form of Ohm’s law is the most conceptually accessible to students. Point out that basically, it says “when there is a strong voltage, the current will be high. But when there is a lot of resistance, that will cause the current to be low.” Current flow is controlled by both these factors.

## Slide 21
Ohm’s law
  You must use consistent SI units (amps, volts, and ohms) for the equation to be valid.
  Ohm’s “law” is not really a law: it’s a mathematical relationship closely obeyed by most conducting materials.
Notes: Ohm’s law is description of the relationship between V, I and R in most materials. Some materials, such as semiconductors, are not “ohmic”.

## Slide 22
Three ways to use Ohm’s law
Determine the current through a resistor.
Determine the voltage drop across a resistor.
Determine the resistance of an unknown resistor.
Notes: Point out to students that these three equations are just a single equation, rearranged.
In fact, Ohm’s law is even more useful than the slide implies, since it can be used for a single resistor, or for any arrangement of resistors.

## Slide 23
Units of resistance
The unit of resistance is the Ohm, Ω.
This form of Ohm’s law can help you remember what an Ohm is:
An ohm is a volt per amp.

## Slide 24
Applying Ohm’s law
What is the current through a 10 Ω resistor when a voltage of 5 V is applied across it?
Notes: Answer on next slide

## Slide 25
Applying Ohm’s law
What is the current through a 10 Ω resistor when a voltage of 5 V is applied across it?
Notes: Preview: In a few minutes, the students will set up this circuit and create a current of about 0.5 amps.

## Slide 26
Click this interactive calculator.
Exploring the ideas
Notes: If possible, bring up the live calculator and work through the examples on the following slides with the students.

## Slide 27
Current
5
10
Engaging with the concepts
What is the current through a 10 Ω resistor when it is connected to a 5 V battery?
Notes: Work through a few example problems like these with the students. Answers are on subsequent slides.

## Slide 28
Current
5
10
0.5
Engaging with the concepts
What is the current through a 10 Ω resistor when it is connected to a 5 V battery?
I = 0.5 amps

## Slide 29
To reduce the current, should resistance be increased or decreased?
Current
5
20
If the resistance increases by a factor of two, how does the current change? Current is halved.
What if resistance is halved?
Engaging with the concepts
Notes: Help students see that current is inversely proportional to resistance. If the resistance increases by a factor of three, the current will decrease by one third. Answers are on the next slide.

## Slide 30
To reduce the current, should resistance be increased or decreased? increased
Current
5
0.25
If the resistance increases by a factor of two, how does the current change? Current is halved.
What if resistance is halved?
Current doubles.
20
Engaging with the concepts
Current is half as much.

## Slide 31
What is the voltage drop across a 50 Ω resistor when a current of 0.10 A flows through it?
Voltage
50
0.10
Engaging with the concepts

## Slide 32
What is the voltage drop across a 50 Ω resistor when a current of 0.10 A flows through it? 5.0 volts
Voltage
5.0
50
0.10
Engaging with the concepts

## Slide 33
Voltage
10
2
What is the resistance of this lamp?
Engaging with the concepts
Notes: Students can now answer the question posed earlier in the presentation. The current was 2 amps because the resistance of the lamp was 5 ohms. The answer is shown on the next slide.

## Slide 34
Voltage
10
5
2
What is the resistance of this lamp? 5 ohms
5 Ω
Engaging with the concepts

## Slide 35
How can you measure resistance?
In Investigation 17C you will use Ohm’s law to determine the resistance of a lamp.
Investigation
Notes: Introduce the investigation. They will start by learning to read the resistor code.

## Slide 36
The resistance of a resistor can be determined by the colored bands printed on the resistor.
Reading the resistor code
Start by finding the tolerance band. It is gold or silver, and usually separated from the other bands by a little gap.
Next, start at the opposite end and read off the colors of the three bands.

## Slide 37
Reading the resistor code
The three colored bands give the value of the resistor, using two digits and a multiplication factor.
Notes: The easy way to begin reading a resistor’s code is to find the tolerance band. Once they find it, students should start at the opposite end of the resistor and read off the colors.

## Slide 38
Reading the resistor code
What are the values of these three resistors, in ohms?
Notes: Go through a couple examples with them.
For example: (green brown red) equals 51 x100 ohms = 5100 ohms.
An even simpler way to explain it is that the third band tells them how many zeros to add to the first two digits.

## Slide 39
Reading the resistor code
These resistors have values of 10 Ω, 51 Ω, and 200 Ω.

## Slide 40
Open the experiment file 17C_ResistanceAndOhmsLaw, and then power on the current sensor and connect it to your software.
Construct the circuit shown using one battery, a switch, a current sensor, a 10 Ω resistor, and any necessary wire modules.
Investigation
Part 1: Current through different resistors

## Slide 41
Investigation
Start data collection, close the switch, and record the measured current in the data table.
Repeat the experiment for the 33 Ω and 100 Ω resistors. Tabulate your results for R and I.
Part 1: Current through different resistors

## Slide 42
Investigation
Repeat the experiment for two other resistors using the spring clip module. You will have to read the resistor values using their colored bands. Tabulate your results for R and I.
Part 1: Current through different resistors

## Slide 43
Graph I on the vertical axis and R on the horizontal axis.
What type of curve best fits this data?
Investigation
Questions
Select the best fit
Notes: The assignment sheet that accompanies this lesson includes graph paper that can be used for this investigation. Students can also use page 2 of the SPARKvue file to graph the data. Ask the students, “Which is the independent variable? The dependent?” Remind students to use a linear scale and label the axes with both the name of the variable and its unit.

## Slide 44
Investigation
Questions
Calculate 1/R for each resistor. Make a second graph with I on the vertical axis and 1/R on the horizontal axis to create a linear graph. Fit a line to determine the slope of the data. What is the value of the slope?
What does the slope of this graph represent? Why?
Select linear fit
Determine the slope

## Slide 45
Power on the voltage sensor and connect it to your software. Advance to Page 2 of the SPARKvue file.
Replace the resistor with the bulb and connect the voltage sensor across the bulb.
Investigation
Part 2: Resistance of a light bulb
Notes: In Part 2 of the lab, students determine the resistance of the lamp.
(Note: Be aware that for a lamp, the resistance when it is lit may be different from its resistance when it is not lit. When a filament heats up, its resistance increases. Measuring the resistance of the unlit lamp using the ohmmeter function on a multimeter will yield a lower resistance.)

## Slide 46
Measure the current through and the voltage across the illuminated bulb.
Calculate the resistance of the lamp using Ohm's law:
Investigation
Part 2: Resistance of a light bulb
Notes: In Part 2 of the lab, students determine the resistance of the lamp.
(Note: Be aware that for a lamp, the resistance when it is lit may be different from its resistance when it is not lit. When a filament heats up, its resistance increases. Measuring the resistance of the unlit lamp using the ohmmeter function on a multimeter will yield a lower resistance.)

## Slide 47
Investigation
Questions for Part 2
What is the resistance of the lamp?
Imagine you have a complicated circuit containing many resistors. How can you use Ohm's law to find the resistance of the entire circuit?
Notes: Ask the students to describe in words what they have done to find the resistance of the lamp. A student volunteer can sketch the circuit diagram on the board and explain how the current and voltage are determined.

## Slide 48: Assessment
Which materials listed below are conductors?
  aluminum
  rubber
  copper
  gold
  diamond
Notes: Ask the students to fill in the blank: all of these materials are either conductors or _________?

## Slide 49: Assessment
Which materials listed below are conductors?
  aluminum
  rubber
  copper
  gold
  diamond
Notes: All metals are conductors. Rubber and diamond are insulators. There is a third category: some materials are semiconductors, which are important in building circuit elements like transistors.

## Slide 50: Assessment
Which equation below is incorrect?
A. B. C. D.
Notes: Give students time to work through the four possibilities.

## Slide 51: Assessment
Which equation below is incorrect?
A. B. C. D.
Notes: Give students time to work through the four possibilities.

## Slide 52: Assessment
What is the voltage drop across a 50 Ω resistor when a current of 0.1 A flows through it?
Notes: Give students time to complete the calculation.

## Slide 53: Assessment
What is the voltage drop across a 50 Ω resistor when a current of 0.1 A flows through it?
Use Ohm’s law:

## Slide 54: Assessment
What is the current through a 10 Ω resistor when it is connected directly to a 15 V battery?
Notes: This is the same problem the students have done experimentally.

## Slide 55: Assessment
What is the current through a 10 Ω resistor when it is connected directly to a 15 V battery?
Notes: Step the students through the algebraic steps needed to convert one form of the equation to another.
It is good practice for students to learn to isolate the wanted variable before plugging in numbers.

## Slide 56: Assessment
How do you connect a voltmeter to measure the voltage across a circuit element?

## Slide 57: Assessment
How do you connect a voltmeter to measure the voltage across a circuit element?
  Connect the voltmeter in parallel with the circuit element in order to measure the voltage across it.

## Slide 58: Assessment
Did you successfully demonstrate the use of current and voltage sensors, power supplies, and resistors?
  Yes! You are learning some of the basic skills that all electrical engineers need to know.
Notes: Congratulate the students on the practical skills they are learning.